Reference variables
Version 1: Dr. Ofir Pele
Version 2: Dr. Miri Ben-Nissan
Version 3: Dr. Erel Segal-Halevi

---
References
Reference – two definitions
(a) A pointer that is used like an object.
(b) Alias - alternative name to existing object.

---
References, example (not a useful one)
References, example
(a) A pointer that is used like an object.
(b) Alias - alternative name to existing object.
int i = 10;
int& j = i; // j is a int reference
        // initialized only
        // once !
j += 5; // changes both i and j

---
References, example (not a useful one)
References, example
(a) A pointer that is used like an object.
(b) Alias - alternative name to existing object.
int i = 10;
int& j = i; // j is a int reference // initialized only
        // once !
j += 5; // changes both i and j
int* k = new int();
j = k; // error k is a pointer
j = *k; // ok j and i equals to *k

---
Pointer vs non-const reference
Pointer vs. Reference
	Pointer	Reference
Initialization	Optional	Mandatory
Dynamic	Yes	No
Arithmetic	Yes	No
Always defined	No	Yes
Notation	(*p), p->x	r, r.x
Containers	Yes	No

---
The famous swap
The famous swap
// Wrong version
void swap(int a, int b) {
   int temp = a;
   a = b;
   b = temp;
}
int main() {
   int x=3, y=7;
   swap(x, y);
   // still x == 3, y == 7 !
}
// C++ version
void swap (int &a, int &b) {
   int t = a;
   a = b;
   b = t;
}
// C version
void swap (int *a, int *b) {
   int t = *a;
   *a = *b;
   *b = t;
}

---
Lvalue & Rvalue
Lvalue & Rvalue
Lvalue = Left Value – can appear at left side of =.
        = Located Value – has a fixed memory location.
        Examples: variables, references …
Rvalue = not Left Value. Numbers, temporaries …
int a=1;
a=5; // Lvalue = Rvalue, Ok
a=a; // Lvalue = Lvalue, Ok
5=a; // Rvalue = Lvalue Comp. error
5=5; // Rvalue = Rvalue Comp. error
a+5=7; // Temporary = Rvalue - Comp. error
f(5)=7; // RIDDLE: Is this legal?

---
Lvalue & Rvalue
Lvalue = Left Value – can appear at left side of =.
        = Located Value – has a fixed memory location.
        Examples: variables, references …
Rvalue = not Left Value. Numbers, temporaries …
int a=1;
a=5; // Lvalue = Rvalue, Ok
a=a; // Lvalue = Lvalue, Ok
5=a; // Rvalue = Lvalue Comp. error
5=5; // Rvalue = Rvalue Comp. error
a+5=7; // Temporary = Rvalue - Comp. error
f(5)=7; // .. it depends: we will see soon.

---
R/L value and references
R/L value and references
non-const Reference – only to a non const Lvalue.
const reference – to both Lvalue and Rvalue
int lv=1;
const int clv=2;
int& lvr1=lv;
int& lvr2=lv+1; //error!
int& lvr3=clv; //error!
const int& cr1=clv;
const int& cr2=5+5;

---
R/L value and references
R/L value and references
non-const Reference – only to a non const Lvalue.
const reference – to both Lvalue and Rvalue
int lv=1;
const int clv=2;
int& lvr1=lv;
int& lvr2=lv+1; //error!
int& lvr3=clv; //error!
const int& cr1=clv;
const int& cr2=5+5; // This is useful for
        // Functions arguments

---
A fancy way to pass arguments to function
A fancy way to pass arguments to function
// pass by const ref
void foo (const int &a)
{
   ...
}
// Pass by value
void foo (int a)
{
   ...
}
// Pass by pointer
void foo (int *pa)
{
   ...
}
Avoid copying objects, without allowing changes in their value.

---
Return a reference to variable
Return a reference to variable
class Buffer
{
   size_t _length;
   int *_buf;
public:
   Buffer (size_t l) :
   _length (l),
   _buf (new int [l])
   {
   }
   int& get(size_t i)
   {
      return _buf[i];
   }
};
int main ()
{
   Buffer buf(5);
   buf.get(0)= 3;
}
Return a ref. to a legal variable (e.g. not on the function stack).

---
Summary
Summary
int * func(int *var0, int &var1, int var2);
By pointer
By Value
By reference

---
References - why?
References - why?
- Efficiency – avoid copying arguments
- Enables modifying variables outside a function
- But that can be done with pointers too!
- Everything that can be done with references, can be done with pointers
- But some “dangerous” features of pointers cannot be done (or harder to do) with references
- Easier to optimize by the compiler
- More convenient in many cases (see examples)
- Widely used as parameters and return values

---
Reference – more
Reference – more
- Like with pointers, don’t return a pointer or reference to a local variable
- You can return a pointer or a reference to a variable that will survive the function call, for example:
  - A heap variable (malloc, new, etc.)
  - A variable from a lower part of the stack
  - Globals, static variables and static members of a class

---
void add(Point& a, Point b)
{
// a is reference, b is a copy
a._x+= b._x;
a._y+= b._y;
}
int main()
{
Point p1(2,3), p2(4,5);
add(p1,p2); // note: we don’t send pointers!
    // p1 is now (6,8)
...
}

---
void add(Point& a, const Point& b)
{
   // a is reference,
   // b is a const ref
  a._x+= b._x;
   a._y+= b._y;
}
int main()
{
   Point p1(2,3), p2(4,5);
   add(p1,p2); // note: we dont send pointers!
   	// p1 is now (6,8)
   ...
}
b is Reference => is not copied
b is Const => we can't change it
Important for large objects!

---
Parameter passing
By value	By reference	By const reference
void f (Point x) {…}	void f (Point& x) {…}	void f (const Point& x) {…}
x is copied	x is not copied	x is not copied
Compiler lets f modify x, but changes have no effect outside	f can modify x	compiler does not let f modify x

---
Point& add(Point& a, const Point& b)
{
   // a is reference, b is a const ref
  a._x+=b._x;
   a._y+=b._y;
   return a;
}
int main()
{
   Point p1(2,3), p2(4,5), p3(0,1);
   add(add(p1,p2),p3); // now p1 is (6,9)
  cout << add(p1,p2).getX(); // note the syntax
   ...
}

---
C++ const

---
Const variables – like in c
Const variables – like in c
int * const p1 = &i; // a const
// pointer to an un-const variable
- p1++; // c.error
- (*p1)++; // ok
const int * p2 = &b; // an un-const
// pointer to a const variable
- p2++; // ok
- (*p2)++; // c.error
const int * const p3 = &b; // a const // pointer to a const variable

---
Const objects & functions (1)
Const objects & functions (1)
class A
{
public:
   void foo1() const;
   void foo2();
};
void A::foo1() const
{
}
void A::foo2()
{
}
int main()
{
   A a;
   const A ca;
   a.foo1();
   a.foo2();
   ca.foo1();
   ca.foo2();
    // comp. error
}

---
Const objects & functions (2)
Const objects & functions (2)
class A
{
public:
   void foo() const;
   void foo();
};
void A::foo() const
{
   cout << "const foo\n";
}
void A::foo()
{
   cout << "foo\n";
}
int main()
{
   A a;
   const A ca;
   a.foo ();
   ca.foo();
}
// output
foo
const foo

---
Why?
Why?
Overload resolution, again:
A::foo(A* this)
A::foo(const A* this)

---
Return a const ref. to variable
Return a const ref. to variable
class Buffer {
   size_t _length;
   int *_buf;
public:
   Buffer (size_t l):
   _length (l),
   _buf (new int [l])  {  }
   const int& get(size_t i) const {
      return _buf[i];
   }
};
int main ()
{
   Buffer buf(5);
   buf.get(0) = 3;
        // illegal
  std::cout <<
   buf.get(0);
}
Why?

---
Const objects with pointers – like in c
Const objects with pointers – like in c
void A::foo() const
{
   //_p++;//won’t compile _p->_n++; // this will !
}
int main()
{
   const A a;
  cout <<
      a._p->_n << endl;
   a.foo();
  cout <<
     a._p->_n << endl;
}
class B { public:
   int _n;
};
class A { public:
   B* _p;
   A();
   void foo() const;
};
A::A() : _p(new B) {
   _p->_n = 17;
}
// output
17
18

---
Const objects with references
Const objects with references
class A
{
public:
   int & _i;
   A(int &i);
   void foo() const;
};
A::A(int &i) : _i(i)
{
}
void A::foo() const
{
   _i++;
}
int main()
{
   int i = 5;
   const A a (i);
   std::cout <<
   a._i << std::endl;
   a.foo();
   std::cout <<
   a._i << std::endl;
}
// output
5
6

---
Initialization of const and ref.
Initialization of const and ref.
class A
{
   int& _a;
   const int _b;
public:
   A(int& a);
};
A::A(int& a)
{
   _a = a;
   _b = 5;
}
// compilation error
Const and ref vars must initialized in their declaration (when they are created):
For fields of a class it’s in the initialization list

---
Initialization of const and ref
Initialization of const and ref
class A
{
   int& _a;
   const int _b;
public:
   A(int& a);
};
A::A(int& a)
: _a(a), _b(5)
{
}
class A
{
   int& _a;
   const int _b;
public:
   A(int& a);
};
A::A(int& a)
{
   _a = a;
   _b = 5;
}
// compilation error
// compiles ok

---
mutable
mutable
- mutable means that a variable can be changed by a const function (even if the object is const)
- Can be applied only to non-static and non-const data members of a class

---
mutable: example #1
mutable: example #1
class X
{
public:
  ...
  X() : _fooAccessCount(0) {}
  bool foo() const
   {
      ++_fooAccessCount;
      ...
   }
   unsigned int fooAccessCount() { return _fooAccessCount; }
private:
   mutable unsigned int _fooAccessCount;
};

---
mutable: example #2
mutable: example #2
class Shape
{
public:
  ...
  void set...(...) { _areaNeedUpdate= true; ... }
  double area() const
   {
      if (_areaNeedUpdate) {
        ...
        _areaNeedUpdate= false;
      }
      return _area;
   }
private:
   mutable bool _areaNeedUpdate= true;
   mutable double _area;
};

---
Copy Constructor
Called whenever an object of type T is copied.
Copy Constructor to class T
gets as argument const T&.
Why?