The Standard
C++ Library
Version 1: Dr. Ofir Pele
Version 2: Dr. Erel Segal-Halevi

---
Main Ideas
Main Ideas
Purpose
Flexibility
Efficiency
Simple & Uniform Interface

---
Q: What types can we put
in a template param?
A: Type which models the
requested concept.

---
Concepts - Example
Concepts - Example
Consider:
The user must provide a type that has a less-than operator (<) to compare two values of type T, the result of which must be convertible to a Boolean value
template<typename T> const T& min(const T& x,
    const T& y)
{
   return x < y? x : y;
}

---
Concepts - Example
Concepts - Example
Consider:
The user must provide a type that has a less-than operator (<) to compare two values of type T, the result of which must be convertible to a Boolean value
template<typename T> const T& min(const T& x,
    const T& y)
{
   return x < y? x : y;
}
The problem:
cryptic error messages
from the implementation of the function
instead of a clear error message

---
Concepts – What we would like it to be:
Concepts – What we would like it to be:
Not C++ syntax:
The user must provide a type that has a less-than operator (<) to compare two values of type T, the result of which must be convertible to a Boolean value
template<LessThanComparable T> const T& min(const T& x,
        const T& y)
{
   return x < y? x : y;
}

---
Concepts
Concepts
Concepts are not a yet part of the C++ language,
Currently there is no (standard) way to declare a concept in a program, or to declare that a particular type is a model of a concept
“were not ready” for C++11,C++14,C++17
C++-20 ?

---
Concepts - advanced
Concepts - advanced
gcc has a new mechanism for concept checking.
To activate it define:_GLIBCXX_CONCEPT_CHECKS
Warning: not clear if it helps or not.
Boost library has a Concept Check Library:
http://www.boost.org/libs/concept_check/concept_check.htm
template<typename T> const T& min(const T& x,
const T& y)
{
   BOOST_CONCEPT_ASSERT((LessThanComparable <T>));
   return x < y? x : y;
}

---
Concepts
Concepts
A concept is a list of requirements on a type.
STL defines a hierarchy of concepts for containers,
iterators, and element types.
Concepts for element types include:
Equality Comparable -
types with operator== ,...
LessThan Comparable -
types with operator< ,...
Assignable -
types with operator=
and copy Ctor

---
Concepts
Concepts
Cleanly separate interface from implementation.
Primitives can also conform to a concept.

---
Concepts refinement
Concepts refinement
 Concept B is a refinement of concept A
 Concept B imposes some additional requirements on A
Similar to inheritance.

---
Main Components
Main Components
Algorithms
Containers
Iterators
Function
Objects
Adaptors
Streams
Strings

---
- Holds copies of elements.
- Assumes elements have:
  Copy Ctor & operator =
- The standard defines the interface.
- Two main classes
  - Sequential containers:
    list, vector,....
  - Associative containers:
    map, set ...
Assignable -
types with operator=
and copy Ctor
Containers

---
(see cplusplus website –
     get to know the documentation)
Containers documentation

---
Sequential Containers
Sequential Containers
Maintain a linear sequence of objects

---
Sequential Containers
Sequential Containers
list - a linked list of objects
  1. Efficient insertion/deletion in front/end/middle
vector - an extendable sequence of objects
  1. Efficient insertion/deletion at end
  2. Random access
deque – double-ended queue
  1. Efficient insertion/deletion at front/end
  2. Random access

---
vector<T>
vector<T>
Contiguous array of elements of type T
Random access
Can grow on as needed basis
std::vector<int> v(2);
  v[0]= 45;
  v[1]= 32;
  v.emplace_back(60); //C++11

---
vector<T>
vector<T>
Contiguous array of elements of type T
Random access
Can grow on as needed basis
std::vector<int> v(2);
  v[0]= 45;
  v[1]= 32;
  v.push_back(60);// old style,
 // we will talk about
  // the difference

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
If we inserted n elements we paid:
1+2+1+4+1+1+1+8+…+n =
O(n) + 1+2+4+…+n
        1+2+4+…+n = ?

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
1+2+4+…n = a

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
1+2+4+…n = a
1+2+4+…n+2n =a+2n

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
1+2+4+…n = a
1+2+4+…n+2n =a+2n
1+2(1+2+…+ n)=a+2n

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
1+2+4+…n = a
1+2+4+…n+2n =a+2n
1+2(1+2+…+ n)=a+2n
1+2(a)=a+2n

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
1+2+4+…n = a
1+2+4+…n+2n =a+2n
1+2(1+2+…+ n)=a+2n
1+2(a)=a+2n
a=2n-1

---
emplace_back / push_back
Average Time Complexity
emplace_back / push_back
Average Time Complexity
If we inserted n elements we paid:
1+2+1+4+1+1+1+8+…+n =
O(n) + 1+2+4+…+n =
O(n)
On average an each insertion cost O(1)

---
size and capacity
size and capacity
size
capacity
The first “size” elements are constructed (initialized)
The last “capacity - size” elements are uninitialized

---
size and capacity
size and capacity
- size_type size() const
- size_type capacity() const
size
capacity

---
C++ vs. Java
- Look at cplusplus documentation of vector.
- Look at Java documentation of Vector.
- Differences:
  - Simple class vs. interface and vtable.
  - Simple elements vs. class element.
  - Two accessors (with and without range check) vs. a single accessor

---
Creating vectors
Creating vectors
Empty vector:
std::vector<int> vec;
vector with 10 ints each one of value int()==0:
std::vector<int>	vec(10);
std::vector<int>	vec(10,0); // better
vector with 10 ints with the value of 42:
std::vector<int>	vec(10, 42);

---
Creating vectors
Creating vectors
Empty vector:
std::vector<int> vec;
vector with 10 ints each one of value int()==0:
std::vector<int>	vec(10);
std::vector<int>	vec(10,0); // better
Notice: int() is NOT a default constructor of int. Uninitialized ints (int k;) contain junk.

---
Creating vectors
Creating vectors
Empty vector:
std::vector<Fred> vec;
vector with 10 default constructed Fred objects. i.e: 10 Fred() objects:
std::vector<Fred> vec(10);
vector with 10 non-default constructed Fred objects:
std::vector<Fred> vec(10, Fred(5,7));

---
Creating vectors: C++11
Creating vectors: C++11
vector with different ints inside it:
std::vector<int> vec{1, 5, 10, -2, 0, 3};
vector with different Fred objects:
std::vector<Fred> vec{Fred(5,7), Fred(2,1) }
Or
std::vector<Fred> vec{ {5,7}, {2,1} }

---
Associated types in vector
Associated types in vector
vector<typename T>::
  1. value_type - The type of object, T, stored
  2. reference - Reference to T
  3. const_reference - const Reference to T
  4. iterator - Iterator used to iterate through a vector (how would you write it?)
  5. …
[break in first week]

---
Time complexity
Time complexity
- Random access to elements.
- Amortized constant time insertion and removal of elements at the end.
- Linear time insertion and removal of elements at the beginning or in the middle.
- vector is the simplest of the STL container classes, and in many cases the most efficient.

---
Adding elements
Adding elements
Inserts a new element at the end:
void push_back(const T&)
    - a.push_back(t)
      - equivalent to:
    - a.insert(a.end(), t)
insert is linear time in the beginning or in the middle.
}
amortized constant time

---
Adding elements-C++11
Adding elements-C++11
Construct and insert a new element at the end:
    template<typename… Args>
void emplace_back(Args&&… args)
    1. a.emplace_back(t)
      1. equivalent to:
    2. a.emplace(a.end(), t)
emplace is linear time in the beginning or in the middle.
}
amortized constant time

---
Accessing elements
Accessing elements
Without boundary checking:
- reference operator[](size_type n)
- const_reference operator[](size_type n) const
With boundary checking:
- reference at(size_type n)
- const_reference at(size_type n) const

---
What about checking boundaries only in DEBUG mode? - Linux
What about checking boundaries only in DEBUG mode? - Linux
g++ has a standard library in DEBUG mode, to activate it define _GLIBCXX_DEBUG
   (g++ -D_GLIBCXX_DEBUG …)
stlport is an implementation of the standard library which includes DEBUG mode (havn't checked it myself yet):
http://www.stlport.org/

---
What about checking boundaries only in DEBUG mode? - MS
What about checking boundaries only in DEBUG mode? - MS
In MSVS 2012 Debug build is automatically safe and Release build mode is not
Other versions also have these kind of “Safe STL” modes but might require defining some flags to turn off or on.

---
vector<T>
vector<T>
Contiguous array of elements of type T
We can get the underlining T* pointer:
if size()>0
T* p= &(v[0])
c++11:
    T* p= v.data()

---
vector<T>
vector<T>
Contiguous array of elements of type T
We can get the underlining T* pointer:
if size()>0
T* p= &(v[0])
c++11:
T* p= v.data()
Useful for interfacing with C
or wrappers that work with C
like Matlab’s mex

---
vector<T> v
vector<T> v

---
vector<T> v
vector<T> v
v.shrink_to_fit() // c++11

---
vector<T> v
vector<T> v
v.shrink_to_fit() // c++11
or

---
Associative Containers
Associative Containers
Supports efficient retrieval of elements
(values) based on keys.
(Typical) Implementation:
red-black binary trees
hash-table (added in c++11)

---
Sorted Associative Containers
Sorted Associative Containers
Set
A set of unique keys
Map
- Associate a value to key (associative array)
- Unique value of each key
Multiset
Multimap
Same, but allow multiple values

---
Sorted Associative Containers & Order
Sorted Associative Containers & Order
Sorted Associative containers use operator<
as default order
We can control order by using our own
comparison function
To understand this issue, we need to use
function object
Function
Objects

---
Anything that can be called as if a function.
For example:
- Pointer to function
- A class that implements operator()
- Lambda expressions (c++11)
Function
Objects

---
Example
Example (folder 3)
class c_str_less {
public:
bool operator()(const char* s1,
        const char* s2) {
return (strcmp(s1,s2) < 0);
}
};
c_str_less cmp; // declare an object
if(cmp(“aa”,”ab”))
 …
if( c_str_less()(“a”,”b”) )
Creates temporary objects, and
then call operator()

---
Template comparator example
Template comparator example
template<typename T>
class less {
public:
bool operator()(const T& lhs, const T& rhs)
{ return lhs < rhs; }
};
less<int> cmp; // declare an object
if( cmp(1,2) )
 …
if( less<int>()(1,2) )
 …
Creates temporary objects,
and then call operator()

---
Using Comparators
Using Comparators
// ascending order
// uses operator < for comparison
set<int> s1;
set<int,less<int>> s1; // same
// descending order
// uses operator > for comparison
set<int,greater<int>> s2;

---
Using Comparators
Using Comparators
Creates a default constructed
MyComp object.
set<int,MyComp> s3;
MyComp cmp(42);
set<int,MyComp> s4(cmp);
Use given MyComp object.

---
Why should we use classes
as function objects?
Why should we use classes
as function objects?
- So we get the “power” of classes.
- Examples:
  - Inheritance.
  - To parameterize our functions in run time or in compile time.
  - To accumulate information.

---
Why should we use classes
as function objects?
Why should we use classes
as function objects?

---
Function object example:
dice code example
Function object example:
dice code example

---
Output Iterator
Input Iterator
Trivial Iterator
Forward Iterator
Bi-directional Iterator
Random-Access Iterator
++, input
++, output
++, I/O
++, --, I/O
Pointer
arithmetic
input
Iterators

---
Iterator Types
Iterator Types
- Output: write only and can write only once
- Input: read many times each item
- Forward supports both read and write
- Bi-directional support also decrement
- Random supports random access
(just like C pointer)

---
Iterators & Containers
Iterators & Containers
Bidirectional iterators:
list, map, set
Random access iterators:
vector
Input/output/forward iterators:
iostreams

---
Iterators & Containers
Iterators & Containers
class NameOfContainer {
…
typedef … iterator; // iterator type
iterator begin(); // first element
iterator end(); // element after last
 NameOfContainer<...> c
 …
 NameOfContainer<...>::iterator it;
 for( it= c.begin(); it!=c.end(); ++it)
       // do something that changes *it

---
Iterators & Containers: c++11
Iterators & Containers: c++11
class NameOfContainer {
…
typedef … iterator; // iterator type
iterator begin(); // first element
iterator end(); // element after last
 NameOfContainer<...> c
 …
 for(auto it= c.begin(); it!=c.end(); ++it)
       // do something that changes *it

---
Iterators & Containers: c++11
Iterators & Containers: c++11
class NameOfContainer {
…
typedef … iterator; // iterator type
iterator begin(); // first element
iterator end(); // element after last
 NameOfContainer<...> c
 …
 for(auto& val : c)
       // do something that changes val

---
const_iterators & Containers
const_iterators & Containers
class NameOfContainer {
…
typedef … const_iterator; // iterator type
const_iterator begin() const; // first element
const_iterator end() const; // element after last
 NameOfContainer<...> c
 …
 NameOfContainer<...>::const_iterator it;
 for( it= c.begin(); it!=c.end(); ++it)
       // do something that does not change *it

---
const_iterators & Containers: c++11
const_iterators & Containers: c++11
class NameOfContainer {
…
typedef … const_iterator; // iterator type
const_iterator cbegin() const; // first element
const_iterator cend() const; // element after last
 NameOfContainer<...> c
 …
 for(auto it= c.cbegin(); it!=c.cend(); ++it)
       // do something that does not change *it

---
const_iterators & Containers: c++11
const_iterators & Containers: c++11
class NameOfContainer {
…
typedef … const_iterator; // iterator type
const_iterator cbegin() const; // first element
const_iterator cend() const; // element after last
 NameOfContainer<...> c
 …
 for(const auto& val : c)
       // do something that does not change val

---
const_iterators & Containers
const_iterators & Containers
…
const_iterator cbegin() const;
const_iterator cend() const;
const_iterator begin() const;
const_iterator end() const;
…
iterator begin();
   iterator end();
Note that the begin() and end() methods that
return regular iterator are not const methods.
i.e: if we get a container by const (const ref, ...)
we can't use these methods. We have to use
the methods that return const_iterator
[end of first week]

---
IntBufferSwap example revisted
IntBufferSwap example revisted

---
Iterators & Sequence Containers
Iterators & Sequence Containers
SeqContainerName<...> c;
SeqContainerName<...>::iterator i,j;
- c.insert(i,x) – inserts x before i
- c.insert(i,first,last)
   – inserts elements in [first,last) before i
- c.erase(i) – erases the element that i points to
- c.erase(i,j)
   – erase elements in range [i,j)

---
Iterators & Sequence Containers c++11
Iterators & Sequence Containers c++11
SeqContainerName<...> c;
SeqContainerName<...>::iterator i,j;
c.emplace(i,p1,...,pn):
Constructs and inserts before i an object
with a constructor that gets p1,...,pn
parameters

---
Iterators & other Containers
Iterators & other Containers
insert and erase has the same ideas,
except they keep the invariants of the specific
container.
For example, a Sorted Associative Container
will remain sorted after insertions and erases.

---
Iterators & other Containers
Iterators & other Containers
So what does c.insert(pos,x) does, when c
is a Unique Sorted Associative Container ?
Inserts x into the set, using pos as a hint to
where it will be inserted.

---
Iterators & other Containers: c++11
Iterators & other Containers: c++11
So what does c.emplace_hint(pos,x) does,
when c is a Unique Sorted Associative
Container?
Constructs and Inserts x into the set,
using pos as a hint to where it will be inserted.

---
Iterator validity
Iterator validity
When working with iterators, we have to
remember that their validity can change
What is wrong with this code?
Container<...> c;
...
 for(auto i= c.begin(); i!=c.end(); ++i )
if( f( *i ) ) { // some test
c.erase(i);
}

---
Iterator validity
Iterator validity
Two cases:
list, set, map
  - i is not a legal iterator

---
Iterator validity
Iterator validity
Two cases:
list, set, map
  - i is not a legal iterator

---
Iterator validity
Iterator validity
Two cases:
list, set, map
  - i is not a legal iterator

---
Iterator validity
Iterator validity
Two cases:
list, set, map
  - i is not a legal iterator
- vector
  - i points to the element after
0
1
2
3
4
5
6
7

---
Iterator validity
Iterator validity
Two cases:
list, set, map
  - i is not a legal iterator
- vector
  - i points to the element after
0
1
3
4
5
6
7

---
Iterator validity
Iterator validity
Two cases:
list, set, map
  - i is not a legal iterator
- vector
  - i points to the element after
In either case,
this is not what we want…

---
Iterator validity – second try...
Iterator validity – second try...
Container<...> c;
auto i= c.begin();
while( i!=c.end() ) {
auto j= i;
++i;
if( f( *j ) ) { // some test
c.erase(j);
...
}Works for set, map, list, not vector or deque

---
Iterators & Map
Iterators & Map
Suppose we work with:
map<string,int> dictionary;
map<string,int>::iterator it;
…
it = dictionary.begin();
What is the type of *it ?

---
Iterators & Map
Iterators & Map
Every STL container type Container defines
Container::value_type
Type of elements stored in container
This is the type returned by an iterator
Container::value_type operator*();

---
Iterators & Map
Iterators & Map
Ok, so what type of elements does a
map return?
map<KeyType,ValueType> keeps pairs
  - KeyType key – “key” of entry
  - ValueType value – “value” of entry

---
Pairs
Pairs
template< typename T1, typename T2>
struct pair {
typedef T1 first_type;
typedef T2 second_type;
T1 first;
T2 second;
pair( const T1& x, const T2& y )
: first(x), second(y)
{}
};

---
Map value_type
Map value_type
template< typename Key, typename T,
    typename Cmp = less<Key> >
class map {
public:
typedef pair<const Key, T> value_type;
typedef Key key_type;
typedef T mapped_type;
typedef Cmp key_compare;
};

---
Using map iterator
Using map iterator
map<string,int> dict;
…
for( auto i = dict.cbegin();
 i != dict.cend();
 ++i )
{
cout << i->first << “ “
    << i->second << “\n”;
}

---
Using map iterator
Using map iterator
map<string,int> dict;
…
for( const auto& val : dict) {
cout << val.first << “ “
        << val.second << “\n”;
}

---
Iterators and Assoc. Containers
Iterators and Assoc. Containers
Additional set of operations:
iterator C::find(key_type const& key)
Return iterator to first element with key.
Return end() if not found
iterator C::lower_bound(key_type const& key)
Return iterator to first element greater or equal to key
iterator C::upper_bound(key_type const& key)
Return iterator to first element greater than key

---
- Good functionality, wrong interface
- For example, adaptors of basic containers
with limited interface:
stack<T,Seq>
queue<T,Seq>
Adaptors

---
stack<T,Seq>
stack<T,Seq>
- provides emplace, push, pop, top, size, empty,...
- Notice that unlike java, pop , is not returning a value. i.e: it's a void function.
- The reason (historic with c++-11?):
to make pop return a value it would be either inefficient or wrong: http://www.sgi.com/tech/stl/stack.html#3

---
- Most STL algorithms works on sequences
- Sequences are passed as two iterators:
  - beginning element
  - element one after last
Algorithms depend on iterator type
not on container type
p
q
sequence [p,q)
Algorithms

---
Example – merge documentation
Example – merge documentation

---
copy
copy
template< typename In, typename Out>
Out copy(In first, In last, Out res)
{
  while (first != last)
    *res++ = *first++;
  return res;
}

---
copy
copy
template< typename In, typename Out>
Out copy(In first, In last, Out res)
{
  while (first != last)
    *res++ = *first++;
  return res;
}
What's wrong with this ?
void foo(const vector<char>& v) {
vector<char> v2;
...
copy(v.begin(),v.end(), v2.begin());

---
copy
copy
template< typename In, typename Out>
Out copy(In first, In last, Out res)
{
  while (first != last)
    *res++ = *first++;
  return res;
}
What's wrong with this ?
OUT OF BOUND !
void foo(const vector<char>& v) {
vector<char> v2;
...
copy(v.begin(),v.end(), v2.begin());

---
So how can we copy and insert ?
So how can we copy and insert ?
Solution #1: Use insert explicitly
void foo(const vector<char>& v) {
vector<char> v2;
...
v2.insert(v2.end(),v.begin(),v.end());

---
So how can we copy and insert ?
So how can we copy and insert ?
Solution #2: Use insert_iterator<Container>. In my humble opinion, not so good as it's not so readable):
void foo(const vector<char>& v) {
vector<char> v2;
...
copy(v.begin(),v.end(), insert_iterator<vector<char>>(v2,v2.begin());

---
sort – using operator <
sort – using operator <
template <class RandomAccessIterator>
void sort(RandomAccessIterator first,
        RandomAccessIterator last);
Example usage(the hard way):
sort< vector<int>::iterator >
        (vec.begin(), vec.end());

---
sort – using operator <
sort – using operator <
template <class RandomAccessIterator>
void sort(RandomAccessIterator first,
        RandomAccessIterator last);
Example usage:
sort(vec.begin(), vec.end());

---
sort – using comparator
sort – using comparator
template <class RandomAccessIterator,
        class StrictWeakOrdering>
void sort(RandomAccessIterator first,
        RandomAccessIterator last,
        StrictWeakOrdering comp);
Example usage:
sort(vec.begin(), vec.end(), greater<int>());

---
sort – compile error
sort – compile error
list<int> l(nums, nums+SIZE);
sort(l.begin(), l.end());

---
sort – compile error
sort – compile error
list<int> l(nums, nums+SIZE);
sort(l.begin(), l.end());
list iterators are bidirectional and not random access !

---
g++
g++
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h: In function ‘void std::sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’:
Main.cpp:17: instantiated from here
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2713: error: no match for ‘operator-’ in ‘__last - __first’
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_bvector.h:182: note: candidates are: ptrdiff_t std::operator-(const std::_Bit_iterator_base&, const std::_Bit_iterator_base&)
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h: In function ‘void std::__final_insertion_sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’:
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2714: instantiated from ‘void std::sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’
Main.cpp:17: instantiated from here
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2357: error: no match for ‘operator-’ in ‘__last - __first’
        ...

---
g++
g++
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h: In function ‘void std::sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’:
Main.cpp:17: instantiated from here
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2713: error: no match for ‘operator-’ in ‘__last - __first’
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_bvector.h:182: note: candidates are: ptrdiff_t std::operator-(const std::_Bit_iterator_base&, const std::_Bit_iterator_base&)
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h: In function ‘void std::__final_insertion_sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’:
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2714: instantiated from ‘void std::sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’
Main.cpp:17: instantiated from here
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2357: error: no match for ‘operator-’ in ‘__last - __first’
        ...
???

---
g++
g++
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h: In function ‘void std::sort(_RandomAccessIterator, _RandomAccessIterator) [with _RandomAccessIterator = std::_List_iterator<int>]’:
Main.cpp:17: instantiated from here
/usr/lib/gcc/i486-linux-gnu/4.1.2/../../../../include/c++/4.1.2/bits/stl_algo.h:2713: error: no match for ‘operator-’ in ‘__last - __first’
        ...

---
g++ -D_GLIBCXX_CONCEPT_CHECKS
and STLFilt
g++ -D_GLIBCXX_CONCEPT_CHECKS
and STLFilt
BD Software STL Message Decryptor v2.47a for gcc
stl_algo.h: In function ‘void sort(_List_iterator<int>, _List_iterator<
        int>)’:
Main.cpp:17: instantiated from here
stl_algo.h:2713: error: no match for ‘operator-’ in ‘__last - __first’
stl_algo.h: In function ‘void __final_insertion_sort(
        _List_iterator<int>, _List_iterator<int>)’:
stl_algo.h:2714: instantiated from ‘void sort(
        _List_iterator<int>, _List_iterator<int>)’
Main.cpp:17: instantiated from here
...

---
g++ -D_GLIBCXX_CONCEPT_CHECKS
and STLFilt
g++ -D_GLIBCXX_CONCEPT_CHECKS
and STLFilt
...
Main.cpp:17: instantiated from here
boost_concept_check.h:223: error: conversion from ‘
    bidirectional_iterator_tag’ to non-scalar type ‘
    random_access_iterator_tag’ requested

---
Cryptic error messages
Cryptic error messages
STLFilt:
An STL Error Message Decryptor for C++:
http://www.bdsoft.com/tools/stlfilt.html

---
Cryptic error messages
Cryptic error messages
Different compilers:
clang++ (free)
intel c++ (not free)